## Slide 1: RANS Turbulence Modeling Sensitivity of Parachute-like Bodies
Logan Halstrom
3/16/17

## Slide 2: Motivation
Orion parachutes can exhibit pendulum motion
  During two-chute failure mode
  Unstable motion
  Potential hazard to crew/vehicle

## Slide 3: Motivation
Use CFD to model dynamic motion
  High-fidelity, rigid geometry model

## Slide 4: Goals
No turbulence model study has been performed for chute
  Run simulation with SST and SA models, compare results
  Develop simple test model
    Coarse grid, low-fidelity geometry: reduce computational demand
    Future use as sandbox for parachute simulations
2,000,000,000 points
3,200,000 points

## Slide 5: OVERFLOW CFD Tool
Structured, overset grids
  Interpolation between overlapping grids
Implicit, Navier-Stokes, finite-differencing
  SSOR, BDF2, etc
Dual-time stepping
  Unsteady solution from physical time stepping
  Converge between time steps with steady-state “sub”-iteration
    Helps pre-condition low-Mach cases
Multi-species gas continuity equation capability
  High-Mach flows (super and hyper sonic)
  Reactive flows (thrusters, etc) but no chemistry
Geometry Manipulation Protocol
  Easy relative grid motion/interpolation
  Primary reason for using OVERFLOW for this simulation

## Slide 6: Turbulence Models
Spalart-Allmaras (SA)
  One-equation: solve for viscosity-related variable (TKE)
  2nd-order Backward Differentiation Formula in OVERFLOW
Shear-Stress Transport (SST)
  Combines best characteristics of traditional two-equation models
    Convection equation: account for energy of turbulence
    Dissipation equation: account for scale of turbulence
  Use k-ω for inner boundary layer
    No need for damping functions
  Use k-ε for freestream
    Not as sensitive as k-ω
  Successive Symmetric Over Relaxation (SSOR) in OVERFLOW

## Slide 7: Run Parameters
Match hemisphere run parameters to high-fidelity chute
  Match flight parachute geometry scale (Lref)
  Scale up flight Mach number x5 (enhance low-Mach convergence)
  Preserve flight Reynolds number

## Slide 8: Grid Development
Use same overset grid strategies as high-fidelity chute
  Cascading box grids propagate flow around body
  Chute box compensates for inadequate, concave near-body grids

## Slide 9: Results: Convergence
Co-plot results show nearly identical convergence
One possibility: solution is independent of turb. Model
Another possibility: solution is more dependent on grid

## Slide 10: Results: Flow
Grid dependency observable in flow behavior
  Flow is better resolved/constrained in near-body grids
  Discontinuities at grid interpolation regions
High-fidelity solution
Hemisphere solution
Hemisphere wireframe

## Slide 11: Results: Wake
Sample x-velocity in wake at spanwise stations
  Results overlap: no influence from turb. Model
    Differencing results reduces to floating point error
  Discontinuities due to bad grid interpolation
Drag Coefficient
  CFD: 3.2, Experiment (semicircle): 2.3
  Possible causes: 2D vs 3D, massive separation, grid
Wake velocity sample locations

## Slide 12: Conclusions and Next Steps
Turbulence study inconclusive
  Solutions were independent of turbulence model BUT…
  Obvious dependency on grid resolution, need refinement studies
Future work
  Testbed for 6DoF pendulum simulations
  Avenue for further grid refinement and turbulence studies

## Slide 13: Other Models (Not RANS)
Compressible LES coupled with FSI
  Supersonic MSL parachute (Karagiozis, Et al.)
  Stretched-vortex model
    Flow in cell assumed to result from straight, axisymmetric vortices aligned with local strain